ProPlas® Bamboo Barrier Film

Installation:

Most bamboo will be sufficiently contained using a 24" deep barrier.

Determine the extent of the area to be given over to the bamboo. Dig a trench around the entire area 
and place the barrier inside.

1. Join the two ends together in a butt joint (with no overlap) with the sealant tape and place the side with the sealant tape to the outside of the hole. If the tape side is facing the root ball it is possible for the rhizomes to travel along the ridge formed by the tape and be diverted below the bottom of the barrier.

2. Another method of joining is to overlap the ends of the barrier by 4 feet and apply a sealant tape vertically on inside and outside of planting area. (Recommended Method)

3. Place the top edge of the barrier approximately 1 inch above the finish grade. This will deter 
overgrowth and make annual maintenance easier.

Plant according to the standard bamboo nursery planting directions paying attention to soil 
deficiencies, drainage and compaction. Be sure the planting area still drains well or the root
system will rot.

Maintenance:

Annual maintenance is a key to controlling bamboo even with a root barrier. 
Rhizomes spread outward from the center of the plant in late spring, summer and fall. Each December when rhizome activity has ended clear the top edge of the barrier and inspect for any rhizome over-growth. If any rhizomes have gone over the top of the barrier cut them off and pull them out of the ground. If this procedure is done annually the rhizome are new, soft and easy to remove.