Densetec Marine Board

Densetec Marine Board is specially formulated to withstand the rigors of harsh outdoor marine environments. It is UV-stabilized to resist damage and retain its beauty, even after years of direct sunlight. Increasingly, Densetec Marine Board is replacing wood and laminates in boating applications. It does not splinter,crack, delaminate, rot, swell, or absorb water like traditional materials. Even under heavy foot traffic on yacht decks, it remains virtually maintenance-free. In addition, there is no need to stain or paint Densetec Marne Board every few years. The color is integrated with the polymer and retains its vibrant appearance better than painted wood.

Fabricating and finishing are easy with standard woodworking tools. Densetec Marine Board forms easily for smooth curves and bends. Since there is no grain pattern, parts can be cut from any part of the sheet virtually eliminating waste for greater economy than wood.

- UV stabilized to withstand harsh marine environments

- Does not splinter, crack or delaminate, rot, swell or absorb water

- Stain resistant and never needs painting

- Machinable with standard wood working tools

- Easily formable for curves and bends

|  Cabinets and counter tops  Doors and windows  Swimming pool equipment  Swim platforms  Trim and molding | Steps and ladder tread Railing Bait tank covers Hatch covers Accessories |
| --- | --- |

| Thicknesses: 1/4" thru 1-1/2" | Widths & Lengths: 54"x96". Other sizes available upon request. |
| --- | --- |

| Polar White | Seafoam | Sand Shade | Light Gray | Dolphin Gray | Black |
| --- | --- | --- | --- | --- | --- |

Desert Sand

| DENSETEC MARINE BOARD LW® - 25% lighter than standard marine board. Lighter, lower cost and easier to handle. |  |  |
| --- | --- | --- |
| DENSETEC TREDSAFE® - An ideal material for use as decking in boats or anywhere else an anti-skid surface is a requirement for a safe walkway or platform, especially effective in wet conditions. Available in two embossed finishes. |  |  |
|  | Diamond | Round |

Call Professional Plastics at (800) 966-7767 or

E-Mail sales@proplas.com

Order Online at www.professionalplastics.com