Perforated Plastic Sheet (standard 48” x 96” sheets)
Professional Plastics offers 23 standard plastic perforated sheets including both dark gray PVC and natural color polypropylene plastic items. Stock sheets range from 1/16" to 1/4" thick, and come in configurations ranging from 10% open air to 48% open air.

Perforated Plastic is ideally suited to many of the same applications as perforated metal; however, it is lighter and is more corrosive resistant. Consider plastic on your next perforated project!

|  | 3/32" diameter 3/16" staggered centers 32 holes per sq. inch 25% open area 1/16 & 1/8" thick |
| --- | --- |
|  | 1/8" diameter 3/16" staggered centers 33 holes per sq. inch 40% open area 1/16 & 1/8" thick |
|  | 1/8" diameter 1/4" staggered centers 18.5 holes per sq. inch 23% open area 1/8" & 3/16" thick |
|  | 3/16" diameter 5/16" staggered centers 12 holes per sq. inch 32% open area 1/8" & 3/16" thick |
|  | 3/16" diameter 1/2" straight line centers 4 holes per sq. inch 10% open area 1/8" & 1/4" thick |
|  | 1/4" diameter 1/2" straight line centers 4 holes per sq. inch 20% open area 1/8" & 1/4" thick |