| Inside Diameter (inches) Wall Thickness (inches) Standard Wall Thin Wall Lightweight wall Frac. Size Min. Nom. Max Nom. Tol. Nom. Tol. Nom. Tol. 1/8 0.120 0.125 0.130 0.020 +/- .004 0.015 +/- .003 - - 1/8 0.125 0.130 0.135 - - - - 0.008 +/- .002 3/16 0.188 0.192 0.198 0.020 +/- .004 0.015 +/- .003 0.010 +/- .003 1/4 0.250 0.255 0.260 0.020 +/- .004 0.015 +/- .003 0.010 +/- .003 5/16 0.313 0.321 0.332 0.020 +/- .004 0.015 +/- .003 0.012 +/- .003 3/8 0.375 0.387 0.394 0.025 +/- .005 0.015 +/- .003 0.015 +/- .005 7/16 0.438 0.451 0.458 0.025 +/- .005 0.018 +/- .004 0.018 +/- .005 1/2 0.500 0.515 0.520 0.025 +/- .005 0.018 +/- .003 0.018 +/- .005 5/8 0.625 0.643 0.650 0.025 +/- .005 0.020 +/- .004 0.020 +/- .005 3/4 0.750 0.772 0.775 0.030 +/- .006 0.025 +/- .005 0.020 +/- .005 7/8 0.875 0.902 0.927 0.035 +/- .007 - - - - 1 1.000 1.030 1.060 0.035 +/- .007 - - - - 1-1/4 1.250 1.287 1.325 0.040 +/- .007 - - - - 1-1/2 1.500 1.550 1.580 0.045 +/- .007 - - - - |  |
| --- | --- |
| Industrial Specification Tubing (inches) |
| Spec'd by ID / OD |
| Frac Sizes | I.D. | Tol. | O.D. | Tol. | Nom. Wall Thickness |
| 1/32 | 0.031 | +/- .004 | .063 | +/- .004 | .015 |
| 1/16 | 0.063 | +/- .005 | .125 | +/- .005 | .030 |
| 3/32 | 0.094 | +/- .005 | .156 | +/- .005 | .030 |
| 1/8 | 0.125 | +/- .005 | .188 | +/- .005 | .030 |
| 3/16 | 0.188 | +/- .005 | .250 | +/- .005 | .030 |
| 1/4 | 0.250 | +/- .005 | .313 | +/- .005 | .030 |
| 5/16 | 0.313 | +/- .005 | .375 | +/- .005 | .030 |
| 3/8 | 0.375 | +/- .005 | .438 | +/- .005 | .030 |
| 7/16 | 0.438 | +/- .005 | .500 | +/- .006 | .030 |
| 1/2 | 0.500 | +/- .006 | .563 | +/- .006 | .030 |
| 9/16 | 0.563 | +/- .006 | .625 | +/- .006 | .030 |
| 5/8 | 0.625 | +/- .006 | .688 | +/- .006 | .030 |
| 11/16 | 0.688 | +/- .006 | .750 | +/- .006 | .032 |
| 3/4 | 0.750 | +/- .006 | .830 | +/- .006 | .040 |
| 7/8 | 0.875 | +/- .006 | .965 | +/- .006 | .045 |
| 1 | 1.000 | +/- .010 | 1.10 | +/- .010 | .050 |
| 1-1/8 | 1.125 | +/- .015 | 1.215 | +/- .015 | .045 |
| 1-1/4 | 1.250 | +/- .015 | 1.340 | +/- .015 | .040 |
| 1-1/2 | 1.500 | +/- .015 | 1.580 | +/- .015 | .040 |

Packaging

Coils of random production lengths. Fractional and Industrial tubing sizes 7/8" and larger are cut lengths 8 to 9 feet.
Custom Packaging on request.

Applicable Specifications

PTFE SW-AMS 3653, ASTM D 3295 MIL-I-22129
PTFE TW-AMS 3655, ASTM D 3295
PTFE LW-AMS 3654, ASTM D 3295
PTFE IND-ASTM D 3295

On all cases of military or commercial specifications, latest revisions apply. Supplied in natural unless otherwise specified. Mil Std. 104 colors on request.

PROFESSIONAL PLASTICS, INC.

(800) 966-7767

www.professionalplastics.com

sales@proplas.com